## Slide 1
Kate MacNamee, MS
Human Error Frameworks – How to think about errors

## Slide 2: What is Human Error
This topic has already been covered, but as a quick reminder we are talking about:
Any action executed by one or more people leading to a deviation from intention, expectation, or desirability

## Slide 3: Errors are often categorized using frameworks
Frameworks are constructs - convenient ways to attempt to organize complex information
  In numerous cases, frameworks may need to be adjust to be a true fit the issue you’re trying to solve
  Some frameworks assess the error in a limited system (e.g., human and device)
  Others asses the errors within a broader systemic context
Different frameworks may be more appropriate than others, depending on the why and how you intend to use them
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 4: Some frameworks delineate between errors and violations
Error
  Unintended action or decision
Violation
  Deliberate deviation from rule or procedure
Psychologists and good designers would suggest that violations also fall into the category of error

## Slide 5: Some frameworks delineate between errors and violations
Human
Failure
Violation
Error
Knowledge based
Rule
based
Skill
based
Routine
Situational
Exceptional
Optimizing
Individual
Diagram adapted from DO - 10.21125/inted.2016.0391

## Slide 6: Some frameworks start with intent (this can manifest in problematic ways)
Human
Failure
Unintended outcome/action
Intended outcome/action
Slip
Lapse
Mistake
Violation
Diagram developed by
TUV Rheinland/Ristek
We knowingly
break from
the rules
Believe we have done the right
thing, but are
wrong
We forget to do
Something; our memory fails
We do the wrong thing by accident; our attention fails
Notes: Dotted line indicates the group of concepts that are “basic error types”

## Slide 7: Some frameworks start with intent (cont.)
Be starting with intention, it implicitly suggests user responsibility
  Do we need to design systems to guard against misuse?
    YES
It favors systems that assumes the “happy path” is the right path
  We can call this development arrogance
  The ideal workflows in a vacuum vs in a system may be completely different
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 8: Broadly speaking…
Whether intended or not, errors and violations are often the result of suboptimal design
We can’t design a better human, so why focus on intention?
We may be better off focusing on how people already function and design our systems around that
Notes: Not because people are special and delicate and need to be catered to, but because it’s literally the path of least resistance

## Slide 9: This model serves as a hybrid between intention and goal-based frameworks
Diagram adapted from: https://www.dpadvantage.co.uk/2019/06/12/human-data-errors/
Human
Failure
Deliberate
Unintentional
Cognition
Error
Execution
Error
Slip
(attention)
Lapse
(memory)
Knowledge
based mistake
Deliberate
deviations from
the process
Rule
based mistake

## Slide 10: Some flavors attempt to reframe intention and goal-aligned vs goal-opposed
Planning/Thinking errors
  Typically unintentional
  Users misunderstood the higher-level concept or the context in which they were working
  Assumes error is often unnoticed unless consequences arise
Execution errors
  Typically unintentional
  Often noticed or noticeable
  Typically assumes the individual knew (or should have known) the right thing to do, but did not manage to do it.
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 11: Still other frameworks start to split out top-down and bottom-up or two-way use issues
Planning failures
Execution failures
Knowledge
-based
Rule-based
Lapse
Slips
Attention:
- Reversal
- Misordering
- Mistiming
- Interference
- Double capture
- Misperception
Memory:
- Omission
- Repetitions
- Reduced intenti-onality
Rule application:
- Applied good
rule to wrong
context
- Applied bad
rule
Cognitive biases:
- Confirmation bias
- Anchoring
- Selectivity
- Vagabonding
- Encystment
Diagram adapted from: https://www.skybrary.aero/articles/human-error-types

## Slide 12: A common framework in Usability/UX/HFE is the Perception-Cognition-Action model
Focuses on the full range of the human side of Human-system interface
Does not inherently account for intent
Helps development teams and designers understand where to focus fixes to reduce risk of harm
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 13: Semi-detailed PCA model (manufacturing example)
Human Error
Perception
Cognition
Action
Omissions
Task not assigned
Wrong point
in time
Inverted order
Wrong amount
of repetitions
Types and
quantities
States
Motion
Incorrect
selection
Incorrect
detection
Incorrect
holding
Incorrection
positioning
Execution
direction
Incorrect
count
Error in risk
perception
Wrong
amount
Unstable
fixation
Incorrect
adjustment
Insufficient
prevention
Figure adapted from doi: 10.1016/j.procir.2016.07.080

## Slide 14: Simplified PCA model (med device example)
Diagram from MacNamee (2020) https://doi.org/10.2345/0899-8205-54.1.28

## Slide 15: Examples of P, C, and A errors
Accidental button press
  Action error: saw the button and knew it was there, but hit it during an unrelated, correct action
  Perception/Sensation error: Didn’t see or feel the button’s presence, so engaged with it as part of an unrelated, correct action
Released syringe plunger before dose is complete
  Action error: finger slipped off the plunger unintentionally
  Perception error: perceived the plunger to have reached the bottom of the syringe/dose window
  Cognition error: misremembered the instructions saying to push the plunger down for 6 seconds instead of 10 seconds
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 16: The reason to categorize errors in the first place is to understand why they occurred
Confusion or misunderstandings that never lead to incorrect actions aren’t of high concern
Understanding why an error occurred (i.e., identifying the root cause) allows us to better prevent that error
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 17: So, is there a “right” framework?
There’s usually an optimal choice, but the best option may change in differing contexts
  Industry and users
  Resources and ability to collaborate
  Timeline/point in the development process
  Practitioner skill level
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 18: Ensure categories allow for focused and effective “risk control measures” or “mitigations”
Helps product teams to focus on the “root cause” of the error – the ultimate reason it happened
Proper identification of root cause means better mitigation, and therefore less likely errors will occur in the future
Notes: Use the notes as needed for talking points or notes for students to consider

## Slide 19: Create or choose a framework by thinking through your context and your goals
Are there principles you believe to be true?
  e.g., The user isn’t to blame
  e.g., Sensation, perception, and cognition affect behavior
  e.g., Attention mediates most human choices
How complex is the use environment or product ecosystem?
What job or goal do you have? Does your team have? Are all disciplines’ goals satisfied?
Notes: Use the notes as needed for talking points or notes for students to consider